## Slide 1
EMBEDDED SYSTEMS · PROJECT BRIEF · 2026
MORSE
COMMUNICATOR
Bidirectional Infrared Morse Messaging Terminal
PREPARED BY
Nour Waleed · Hagar Ali
INSTRUCTOR
Dr. Alaa Hamdi
> SYSTEM ONLINE · AWAITING SIGNAL

## Slide 2
00 · TABLE OF CONTENTS
What we'll cover.
Eight chapters from concept to working prototype.
01
Overview
What the system does
02
Objectives
What we set out to build
03
Hardware
Components & pin map
04
Button Layer
Input mechanics
05
Software
Code architecture
06
Pipeline
End-to-end data flow
07
Sim vs HW
Where they diverge
08
Issues Fixed
Real-world debugging
02 / 12
● INDEX · 08 CHAPTERS

## Slide 3
01 · PROJECT OVERVIEW
Two-way Morse, over light.
01 THE SETUP
Two identical Arduino terminals. Each can send and receive Morse-encoded text through an infrared link.
02 THE INTERACTION
Six dedicated buttons compose letters. The system decodes Morse locally, transmits the message, and shows the chat on a 16×2 LCD.
2
STATIONS
6
BUTTONS / SIDE
36
MORSE GLYPHS
03 / 12
▸ CLICK TO REVEAL

## Slide 4
02 · OBJECTIVES
Five goals.
Every objective is verifiable on the hardware.
01
BUILD
Bidirectional embedded comms with two identical stations.
02
CONVERT
Morse button input → readable English text before transmission.
03
TRANSMIT
Send data over IR; reconstruct it accurately on the receiver.
04
RESPOND
Same firmware handles both send and reply on either side.
05
DISPLAY
Show latest chat history on the LCD for live demo + validation.
04 / 12
▸ CLICK TO REVEAL
● OBJECTIVES · 5 VERIFIED

## Slide 5
03 · HARDWARE
Bill of materials.
2×
Arduino Uno
Main controllers
2×
VS1838B
IR receiver
2×
IR LED
Emitter + resistor
2×
16×2 LCD
I²C @ 0x27
2×
Buzzer
Tone feedback
12×
Push Button
6 per station
PIN MAP
DOT
D4
DASH
D5
END
D6
BACK
D7
SPACE
D8
SEND
D9
BUZZ
D10
IR TX
D3
IR RX
D11
SDA
A4
SCL
A5
05 / 12
▸ CLICK TO REVEAL

## Slide 6
04 · BUTTON LAYER
Six buttons. One language.
No keyboard. No screen typing. Pure Morse composition.
.
DOT
Append a dot
PIN D4
—
DASH
Append a dash
PIN D5
↵
END
Decode → letter
PIN D6
⌫
BACK
Edit current
PIN D7
␣
SPACE
Word gap
PIN D8
▶
SEND
Transmit via IR
PIN D9
06 / 12
▸ CLICK TO REVEAL
● INPUT INTERFACE · 6 BTN

## Slide 7
05 · SOFTWARE ARCHITECTURE
Modular firmware.
One sketch runs on both stations — symmetric design.
setup()
Init pins, LCD, buzzer, IR.
loop()
Continuous: buttons + receive.
checkButtons()
Debounced, one-shot detection.
handleButton(i)
Action dispatch by button.
decodeMorse()
Code → English char (or null).
sendMessageIR()
Char-by-char NEC transmission.
checkReceive()
Rebuild incoming → end marker.
updateLCD()
Render send mode or chat log.
07 / 12
▸ CLICK TO REVEAL

## Slide 8
06 · EXECUTION PIPELINE
Eight stages, one beat.
From button press to chat history — the message journey.
01
setup()
Boot peripherals
02
loop()
Poll buttons + IR
03
handleButton()
Compose / send
04
sendMessageIR()
Transmit + EOM
05
checkReceive()
Rebuild chars
06
addToLog()
Store in history
08 / 12
▸ CLICK TO REVEAL
● DATA FLOW · 6 STAGES

## Slide 9
07 · SIMULATION vs HARDWARE
Two worlds. Same logic.
What works in Tikercad doesn't always survive the breadboard.
ASPECT
SIMULATION
HARDWARE
ENVIRONMENT
Tinkercad
Two real Arduino boards
MEDIUM
UART
Physical IR LED + receiver
DEBUGGING
Fast iteration, easy rewiring
Wiring checks + alignment
TIMING
Predictable, controlled
Affected by ambient light + blocking code
FAULTS
Only what's modeled
Polarity, weak TX, saturation
VALUE
Verifies logic & UI flow
Proves the full embedded system
09 / 12
▸ CLICK TO REVEAL

## Slide 10
08 · ISSUES & FIXES
What broke. What we did.
Real debugging — every fix is wired into the final code.
BUTTON CONFUSION
Triggered wrong actions, stayed active.
→
APPLIED FIX
Rebuilt button area, aligned signal paths.
BUZZER GHOST FIRES
Activated without input — short or wrong row.
→
APPLIED FIX
Isolated buzzer to clean two-row connection.
IR PROTOCOL MISMATCH
TX sent but RX couldn't rebuild chars.
→
APPLIED FIX
Unified to NEC command-byte workflow.
REPLY PATH INSTABLE
First exchange worked, later replies failed.
→
APPLIED FIX
Reduced blocking; re-armed receiver after TX.
HISTORY TOO SHALLOW
Only minimal chat state visible.
→
APPLIED FIX
Larger log; both sent + received tracked.
10 / 12
▸ CLICK TO REVEAL
● 5 ISSUES · 5 RESOLVED

## Slide 11
09 · TESTING · VALIDATION · LIMITS
It works. Here's how we know.
✓ VERIFIED ON HARDWARE
✓
All six controls respond correctly
✓
Buzzer feedback + LCD updates
✓
One-way IR transmission
✓
Reply transmission (reverse direction)
✓
Repeated exchanges after fixes
✓
Chat history logs both sides
△ KNOWN LIMITATIONS
△
16×2 LCD shows only two lines at once
△
IR depends on distance + alignment
△
History depth bounded by Arduino RAM
△
Letters + digits only (limited punctuation)
11 / 12
▸ CLICK TO REVEAL

## Slide 12
▸ CONCLUSION · PROJECT COMPLETE
Signal sent.
Signal received.
The Morse Communicator delivers a complete embedded workflow: button-based Morse input, local English decoding, infrared transmission, reception, reply, and chat-style history — symmetric across two stations.
100%
OBJECTIVES MET
5/5
ISSUES RESOLVED
2
STATIONS · 1 PROTOCOL
// MORSE COMMUNICATOR · v1.0 · EMBEDDED SYSTEMS · 2026

## Slide 13
EMBEDDED SYSTEMS · PROJECT BRIEF · Bidirectional Infrared Morse Messaging Terminal
Thank
YOU
> SYSTEM OFFLINE · THAT’S IT